Appendix D: IPtables' configuration options

We can configure the compilation process of the iptables' source package to some extent that the script allows us. I'm not going to explore all the details but this is just a copy of the installation notes file.

# ./configure [options]

--prefix=

The prefix to put all installed files under. It defaults to /usr/local, so the binaries will go into /usr/local/bin, sbin, manpages into /usr/local/share/man, etc.

--with-xtlibdir=

The path to where Xtables extensions should be installed to. It defaults to ${prefix}/libexec/xtables.

--enable-devel (or --disable-devel)

This option causes development files to be installed to ${includedir}, which is needed for building additional packages, such as Xtables-addons or other 3rd-party extensions.

It is enabled by default.

--enable-libipq

This option causes libipq to be installed into ${libdir} and ${includedir}.

--enable-static

Enable building single standalone multipurpose binaries, (iptables-static and ip6tables-static), which contain every extension compiled-in (and does not support additional extensions).

--with-ksource=

Xtables does not depend on kernel headers anymore, but you can optionally specify a search path to include anyway. This is probably only useful for development.

If you want to enable debugging, use
# ./configure CFLAGS="-ggdb3 -O0"

(-O0 is used to turn off instruction reordering, which makes debugging much easier.)
The make process will automatically build multipurpose binaries. These have the core (iptables), -save, -restore and -xml code compiled into one binary, but extensions remain as modules.

If you want to build a statically linked version of the iptables binary, without the need for loading the plugins at runtime (e.g. for an embedded device or router-on-a-disk), you can use the –enable-static configure flag.